## Slide 1: XML and the LIMS-CDS Interface

## Slide 2: The QA/QC Lab Environment
A typical QA/QC Pharmaceutical Lab consists of a LIMS, CDS, Instruments, Storage Chambers, and Samples (in various batches and lots).
In a QA/QC lab, samples are taken from assembly lines and checked for constituents and purity.
LIMS: A LIMS is a Laboratory Information Management System where all sample data is stored, managed and queried.
CDS: A CDS is a Chromatography Data System that interfaces with chromatography instruments like GC/LC and is used for analyzing the data.

## Slide 3: The Interface
Since the LIMS is central repository of data in the Lab, it needs to get input about the chromatography results from the CDS.
LIMS needs to send sample data to the CDS and receive results.
Implemented the interface using a DTD.

## Slide 4: LIMS Export/CDS Import
The LIMS Export module runs in two modes
  UI Mode: VB
  Command-line mode: CP macros
The Cerity Import module is written in VB/VC and uses ADO/MSXML.

## Slide 5: CDS Export/LIMS Import
The CDS Export module is written in VB/VC and uses ADO/MSXML
The LIMS Import module is written in C++ and uses the (Apache-IBM) Xerces parser.

## Slide 6: Experiences
Type Checking
NULL Values
Data Constraints
Mapping Issues
Configuration Issues
E-signature issues
Finalizing the DTD
Binary Data Transfer

## Slide 7: XML and Datatypes
No way to specify data type in DTD/XML other than PCDATA and CDATA
Validating XML data can take one of the 2 approaches
  Add data type information in the DTD.
    Makes the XML more stringent
    No ambiguity in data interpretation
  Add the type checking logic in the import/export modules.
    XML is no more self-contained
    More time & effort spent by the developer

## Slide 8: NULL Values
NULL values in the database need to be handled carefully.
Empty elements or attributes are NOT NULL. They are blank/empty strings.
Missing elements or attributes indicate NULL values.

## Slide 9: Data Constraints
Difficult to express data constraints in a DTD.
E.g.
  Domain constraint:
    May specify allowable values for an attribute, but not for an element
    Not possible to define domain sets for both attributes and elements.

## Slide 10: Mapping Issues
With export/import modules multiple mapping issues arise:
  Mapping terms from one system to the other
    Needs considerable domain and system expertise.
  The relationships between terms in different systems may vary
  Relations that are 1:N in one system may turn out to be M:N in other systems

## Slide 11: Configuration
The export/import modules necessarily need configuration information in additional to the XML interface.
Configuration is required
  To provide data for the XML (e.g. DTD version)
  To provide for minimal data entry by the user. The data is already present in one system. We need to tell the export module where to pick it up from.
  To provide seed information for the export and import. Seed information includes information to initialize running numbers.

## Slide 12: Configuration (cont.)
  To provide some data that controls the behavior of the export/import modules. E.g. Information to control if the file needs to contain checksum information.
  To provide for mapping information.
  To provide for file transfer information.

## Slide 13: E-signature Issues (21 CFR Part 11)
The files need to be protected against tampering. Additional checksum information is required with the files.
Username and timestamps need to be in the files.
It is not possible to provide ‘signed’ files in case of background export/import processes.
It is not possible to stamp approvals from one system to another unless usernames and statuses (e.g. reviewed, peer reviewed, approved) are synchronized.

## Slide 14: Finalizing the DTD
Takes a very long time for the DTD to be finalized.
Difficult to prove that the DTD/XML are necessary and sufficient.
  Some unintended variants may be derived from the DTD.

## Slide 15: Binary Data Transfer
Some labs need to transfer binary data like chromatograms. As of today, there is no support for Binary Data Transfer. (There is a pending proposal for XML-MIME, XMTP, base64).
Vector data can be transferred, but there is no support for raster/bitmap data.
Also, there is no support for markup within markup.

## Slide 16: References