## Slide 1: Universal Plug and Play (UPnP) and XML
Shridhar Bhat
bhat@pspl.co.in

## Slide 2: Motivation
XML can be used in innovative ways to achieve platform independent and flexible application-layer protocol communication

## Slide 3: UPnP Architecture
Internet
Network2
Network1
Control Point
(Manager)
Device1
Device2
Fig.1: Typical Universal Plug and Play system architecture

## Slide 4: UPnP Terminology
Addressing
  IP address binding
Discovery
  advertisements by the devices
  search requests from the control points
Description
  stuff to be advertised
Control
  requests for actions from the control points to the devices
Eventing
  subscription for events by the control points
  notification of events by the device
Presentation (control point)
  GUI to the user by the control point

## Slide 5
Addressing
DHCP
Auto-IP
Network
Device code
Description
Events generated
by the device
Events notification
Eventing
Event
subscription
Control
Control
Request
Control
Response
Action
Request
Action
Response
Discovery
Device
Advertisements
over SSDP channel
Discovery
Search
Device side of the UPnP Subsystem

## Slide 6
Control Point side of the UPnP Subsystem
Addressing
DHCP
Auto-IP
Network
Discovery
Search
Discovery
Response
Discovery
Control
Request
Control
Eventing
Event
subscription
Events notification
Control
Response
Presentation
Control point user

## Slide 7: Description
Device Description
  defines logical devices e.g. VCR
  contains URLs for service description, control, eventing and presentation
  provided during the advertisements
Services descriptions
  e.g. play, rewind, stop etc.
  tells how to form a request for a service
  events that can be subscribed to by control points
  fetched using HTTP GET

## Slide 8: XML in UPnP: Device Description
<xml version="1.0"?> <root xmlns="urn:schemas-upnp-org:device-1-0"> <specVersion> <major>1</major> <minor>0</minor> </specVersion> <device> <serviceList> <service> <serviceType>urn:schemas-upnp-org:service:serviceType:v</serviceType> <serviceId>urn:upnp-org:serviceId:serviceID</serviceId> <SCPDURL>URL to service description</SCPDURL> <controlURL> URL for control </controlURL> <eventSubURL> URL for eventing </eventSubURL> </service> Declarations for other services defined by a UPnP Forum (if any) go here Declarations for other services added by UPnP vendor (if any) go here </serviceList> <deviceList> Description of embedded devices defined by a UPnP Forum (if any) go here Description of embedded devices added by UPnP vendor (if any) go here </deviceList> <presentationURL>URL for presentation</presentationURL> </device> </root>

## Slide 9: XML in UPnP: Service Description
<scpd xmlns="urn:schemas-upnp-org:service-1-0"> <actionList> <action> <name> actionName </name> <argumentList> <argument> <name>formalParameterName </name> <direction> in or out </direction> <relatedStateVariable> stateVariableName </relatedStateVariable> </argument> </argumentList> </action> </actionList> <serviceStateTable> <stateVariable sendEvents="yes"> <name>variableName </name> <dataType> variable data type </dataType> <defaultValue>default value </defaultValue> <allowedValueList> <allowedValue> enumerated value </allowedValue> </allowedValueList> </stateVariable> </serviceStateTable> </scpd>

## Slide 10: Control
Uses Simple Object Access Protocol (SOAP)
Control points
  fetch the URL for control
  construct requests (RPC calls) using SOAP
  send the requests over HTTP
  wait for the SOAP responses from devices
Devices
  parse the SOAP requests
  carry out the required action and return responses in SOAP messages

## Slide 11: XML in UPnP: SOAP
Uses XML and HTTP for RPC calls
SOAP request POST path of control URL HTTP/1.1 HOST: host of control URL:port of control URL CONTENT-LENGTH: bytes in body CONTENT-TYPE: text/xml; charset="utf-8" SOAPACTION: "urn:schemas-upnp-org:service:serviceType:v#actionName” <s:Envelope xmlns: s=“http://schemas.xmlsoap.org/soap/envelope” s:encodingStyle=“http://schemas.xmlsoap.org/soap/encoding”> <s:Body> <u:actionName xmlns:u="urn:schemas-upnp-org:service:serviceType:v"> <argumentName>in arg value</argumentName> other in args and their values go here, if any </u:actionName> </s:Body> </s:Envelope>

## Slide 12: Eventing
Device publishes a list of events for which control points can subscribe and get notifications
Control points subscribe with the devices for the events published
Event notifications by the devices over TCP to control points

## Slide 13: XML in UPnP: Event Notification
NOTIFY delivery path HTTP/1.1 HOST: delivery host:delivery port CONTENT-TYPE: text/xml CONTENT-LENGTH: Bytes in body NT: upnp:event NTS: upnp:propchange SID: uuid:subscription-UUID SEQ: event key <e:propertyset xmlns:e="urn:schemas-upnp-org:event-1-0"> <e:property> <variableName>new value</variableName> </e:property> Other variable names and values (if any) go here. </e:propertyset>

## Slide 14: Why XML?
Platform independence
Communication over HTTP
  penetrates the firewalls without extra efforts
  no need to run services on special ports
Provides the level of expressiveness and extensibility needed to describe devices and their services
forgiving technology :-)

## Slide 15: Challenges Ahead
No consideration for security in the UPnP specification
IP over electric distribution network??
Scarcity of IP addresses
  IPv6

## Slide 16: Competing technology
Jini
  uses Java interfaces instead of XML
  enjoys benefits of object oriented programming
  works at higher level of abstraction
  easier to define interfaces than protocols
  needs JVM, Object serialization and RMI APIs on the devices and control points

## Slide 17: Conclusion
XML can be useful in defining application level protocol communication
XML allows a light-weight implementation for UPnP devices

## Slide 18: References
Universal Plug and Play forum, http;//www.upnp.org
UPnP architecture, http://www.upnp.org/UPnPDevice_Architecture_1.0.htm
Intel’s UPnP SDK for Linux, http://developer.intel.com/ial/upnp/
Simple object access protocol, http://www.w3.org/TR/SOAP/
IETF draft on ‘Multicast and Unicast UDP HTTP Messages’, http://www.ics.uci.edu/pub/ietf/http/draft-goland-http-udp-01.txt

## Slide 19
Questions?

## Slide 20
Thank you
:-)