## Slide 1: CS344: Introduction to Artificial Intelligence (associated lab: CS386)
Pushpak Bhattacharyya CSE Dept., IIT Bombay
Lecture–3: Fuzzy Inferencing: Inverted Pendulum

## Slide 2: Inferencing
Two methods of inferencing in classical logic
  Modus Ponens
    Given p and pq, infer q
  Modus Tolens
    Given ~q and pq, infer ~p
How is fuzzy inferencing done?

## Slide 3: A look at reasoning
Deduction: p, pq|- q
Induction: p1, p2, p3, …|- for_all p
Abduction: q, pq|- p
Default reasoning: Non-monotonic reasoning: Negation by failure
  If something cannot be proven, its negation is asserted to be true
  E.g., in Prolog

## Slide 4: Completeness and Soundness
Completeness question
  Provability - Is the machine powerful enough to establish a fact?
Soundness – Anything that is proved to be true is indeed true
  Truth - Is the fact true?

## Slide 5: Fuzzy Modus Ponens in terms of truth values
Given t(p)=1 and t(pq)=1, infer t(q)=1
In fuzzy logic,
  given t(p)>=a, 0<=a<=1
  and t(p>q)=c, 0<=c<=1
  What is t(q)
How much of truth is transferred over the channel
p
q

## Slide 6: Lukasiewitz formula for Fuzzy Implication
t(P) = truth value of a proposition/predicate. In fuzzy logic t(P) = [0,1]
t( ) = min[1,1 -t(P)+t(Q)]
Lukasiewitz definition of implication

## Slide 7: Use Lukasiewitz definition
t(pq) = min[1,1 -t(p)+t(q)]
We have t(p->q)=c, i.e., min[1,1 -t(p)+t(q)]=c
Case 1:
c=1 gives 1 -t(p)+t(q)>=1, i.e., t(q)>=a
Otherwise, 1 -t(p)+t(q)=c, i.e., t(q)>=c+a-1
Combining, t(q)=max(0,a+c-1)
This is the amount of truth transferred over the channel pq

## Slide 8
Eg: If pressure is high then Volume is low
Pressure/Volume
High Pressure
ANDING of Clauses on the LHS of implication
Low Volume

## Slide 9: Fuzzy Inferencing
Core
The Lukasiewitz rule
t( ) = min[1,1 + t(P) – t(Q)]
An example
Controlling an inverted pendulum
θ
= angular velocity
Motor
i=current

## Slide 10
The goal: To keep the pendulum in vertical position (θ=0)
in dynamic equilibrium. Whenever the pendulum departs from vertical, a torque is produced by sending a current ‘i’
Controlling factors for appropriate current
Angle θ, Angular velocity θ.
Some intuitive rules
If θ is +ve small and θ. is –ve small
then current is zero
If θ is +ve small and θ. is +ve small
then current is –ve medium

## Slide 11
-ve med
-ve small
Zero
+ve small
+ve med
-ve med
-ve small
Zero
+ve small
+ve med
+ve med
+ve small
-ve small
-ve med
-ve small
+ve small
Zero
Zero
Zero
Region of interest
Control Matrix
θ.
θ

## Slide 12
Each cell is a rule of the form
If θ is <> and θ. is <>
then i is <>
4 “Centre rules”
if θ = = Zero and θ. = = Zero then i = Zero
if θ is +ve small and θ. = = Zero then i is –ve small
if θ is –ve small and θ.= = Zero then i is +ve small
if θ = = Zero and θ. is +ve small then i is –ve small
if θ = = Zero and θ. is –ve small then i is +ve small

## Slide 13
Linguistic variables
Zero
+ve small
-ve small
Profiles
-ε
+ε
ε2
-ε2
-ε3
ε3
+ve small
-ve small
1
Quantity (θ, θ., i)
zero

## Slide 14: Inference procedure
Read actual numerical values of θ and θ.
Get the corresponding μ values μZero, μ(+ve small), μ(-ve small). This is called FUZZIFICATION
For different rules, get the fuzzy i values from the R.H.S of the rules.
“Collate” by some method and get ONE current value. This is called DEFUZZIFICATION
Result is one numerical value of i.

## Slide 15
if θ is Zero and dθ/dt is Zero then i is Zero
if θ is Zero and dθ/dt is +ve small then i is –ve small
if θ is +ve small and dθ/dt is Zero then i is –ve small
if θ +ve small and dθ/dt is +ve small then i is -ve medium
-ε
+ε
ε2
-ε2
-ε3
ε3
+ve small
-ve small
1
Quantity (θ, θ., i)
zero
Rules Involved

## Slide 16
Suppose θ is 1 radian and dθ/dt is 1 rad/sec
μzero(θ =1)=0.8 (say)
μ +ve-small(θ =1)=0.4 (say)
μzero(dθ/dt =1)=0.3 (say)
μ+ve-small(dθ/dt =1)=0.7 (say)
-ε
+ε
ε2
-ε2
-ε3
ε3
+ve small
-ve small
1
Quantity (θ, θ., i)
zero
Fuzzification
1rad
1 rad/sec

## Slide 17
Suppose θ is 1 radian and dθ/dt is 1 rad/sec
μzero(θ =1)=0.8 (say)
μ +ve-small(θ =1)=0.4 (say)
μzero(dθ/dt =1)=0.3 (say)
μ+ve-small(dθ/dt =1)=0.7 (say)
Fuzzification
if θ is Zero and dθ/dt is Zero then i is Zero
min(0.8, 0.3)=0.3
hence μzero(i)=0.3
if θ is Zero and dθ/dt is +ve small then i is –ve small
min(0.8, 0.7)=0.7
hence μ-ve-small(i)=0.7
if θ is +ve small and dθ/dt is Zero then i is –ve small
min(0.4, 0.3)=0.3
hence μ-ve-small(i)=0.3
if θ +ve small and dθ/dt is +ve small then i is -ve medium
min(0.4, 0.7)=0.4
hence μ-ve-medium(i)=0.4

## Slide 18
-ε
+ε
-ε2
-ε3
-ve small
1
zero
Finding i
0.4
0.3
Possible candidates:
i=0.5 and -0.5 from the “zero” profile and μ=0.3
i=-0.1 and -2.5 from the “-ve-small” profile and μ=0.3
i=-1.7 and -4.1 from the “-ve-small” profile and μ=0.3
-4.1
-2.5
-ve small
-ve medium
0.7

## Slide 19
-ε
+ε
-ve small
zero
Defuzzification: Finding i
by the centroid method
Possible candidates:
i is the x-coord of the centroid of the areas given by the
blue trapezium, the green trapeziums and the black trapezium
-4.1
-2.5
-ve medium
Required i value
Centroid of three
trapezoids