## Slide 1: M.Tech Thesis Presentation

## Slide 2: M.Tech Thesis Presentation WLAN Watch: A Step Towards The Study Of 802.11b Wireless LANs.
Supervisor:
Dr. Pravin Bhagwat
Presented by:
M. Imtiaz ur rahaman

## Slide 3: 802.11b Wireless LANs
802.11b - MAC layer standard for wireless LANs.
WLAN networks found in Airports, Coffee shops, Universities…
Bandwidth : 11Mbps.
Need to STUDY the WLANs.
Suggest possible IMPROVEMENTS.
No adequate TOOLS available.

## Slide 4: What Sort Of Tools?
Error patterns
  Sniff all packets including corrupted ones, map to the original packet - Error Correction.
Signal level range
  Where huge % of packets get corrupted (PPSL).
Critical signal level
  Below which packets are lost (PPSL).
Packet size
  Beyond which most of the packets get corrupted.

## Slide 5: What Sort Of Tools?
Effect Of
  Power, load on AP etc., on packet loss and packet corruption ratio.
Generic
  Support for multiple NICs.
Linux environment

## Slide 6: Existing Tools
Sniffers
  Do not log corrupted packets. Hence do not help in Error Correction.
Signal meters
  Show signal strength of signal received from the AP connected to.
  No per packet information.

## Slide 7: Existing Tools
Low experimentation support
  Can’t conduct experiments with desired traffic.
  Specified packet size, power level, …
No idea about
  Error patterns, packet loss ratio, packet corruption ratio…

## Slide 8: Objectives
Generic Device Driver for 802.11b NICs.
Standardize the Driver-Application Interface.
Build Generic Tools.
Hence, setup a stage to study and suggest any possible improvements in 802.11b WLANs.

## Slide 9: Architecture - Overview
Applications
Kernel
Hardware
TCP/IP
1. Wireless NIC
2. Firmware
4. Driver
5. NIC - INFO
6. ioctls, /proc
3. Interface

## Slide 10: Generic Device Driver
Applications
Kernel
Hardware
1. Multiple Vendors
2. Different Firmwares
4. Generic Driver
5. NIC - INFO
6. Standard API
3. Various Interfaces
Intersil
Cisco
7. Generic Tools

## Slide 11: Generic Device Driver: Issues
Applications
Kernel
Hardware
1. Multiple Vendors
2. Different Firmwares
4. Different Drivers
5. NIC - INFO
6. Proprietary APIs
3. Various Interfaces
Intersil
Cisco

## Slide 12: Generic Device Driver: Issues
Intersil
Cisco
Lucent
PrismII
Symbol
PCMCIA
PCI
PLX
USB
TI
Atmel
MAC - Vendors
Resellers
Interfaces

## Slide 13: Generic Device Driver: Observations
Thought of a generic driver is too ambitious.
Driver maintenance?.
Note: Orinoco driver claims to be generic. Supports : Lucent, PrismII & Symbol cards.
Not fully functional on some PrismII cards.
Recent versions do not handle properly the Symbol cards.
No USB support.
The wlan-ng and HostAP drivers for PrismII cards are more tested & have more features.

## Slide 14: Generic Driver-Application Interface
Applications
Kernel
Hardware
1. Multiple Vendors
2. Different Firmwares
4. Different Drivers
5. NIC - INFO
6. Proprietary APIs
3. Various Interfaces
Intersil
Cisco
7. Standard API
8. Generic Tools

## Slide 15: Driver – Application Interface
Standard API: Wireless Extensions by Jean Tourrilhes
Idea - manipulate any wireless networking device in a standard and uniform way.
Interface and tools:
  /proc/net/wireless – read statistics.
  iwconfig – standard device configuration. Clone of ifconfig.
  iwspy – gather quality information for a set of network addresses.
  iwpriv – device specific.
Drivers supporting Wireless Extensions:
  Wvlan_cs, Lucent (orinoco), PrismII (wlan-ng), HostAP, Cisco (Aironet)

## Slide 16: Driver – Application Interface: Issues
  Modify existing drivers to implement appropriate ioctls and create standard /proc entries.
  Drivers have their own well defined configuration tools. The wlan-ng drivers come with the wlanctl-ng, wlancfg tools.
  New drivers coming into existence do not care to implement the standard API.

## Slide 17: Generic User Space Tools
Applications
Kernel
Hardware
1. Multiple Vendors
2. Different Firmwares
4. Different Drivers
5. NIC - INFO
6. Proprietary APIs
3. Various Interfaces
Intersil
Cisco
7. User Space Library
8. Generic Tool

## Slide 18: WLAN Watch - Overview
Intersil
Cisco
Completely User Space
To pass up corrupted packets
Wlan-ng
airo
Access Point
Root Privileges

## Slide 19: WLAN Watch - Architecture
Ethernet Backbone
Client
sniffer
Server
RFMON
Access Point
START_SNIFFING
00:03:2F:00:E2:8A
6
START_SNIFFING
00:03:2F:00:E2:8A
6
START_SNIFFING
00:03:2F:00:E2:8A
6
UDP Packets
STOP_SNIFFING
STOP_SNIFFING
STOP_SNIFFING
IMPORT_RXLOG
IMPORT_RXLOG
IMPORT_RXLOG
RxLog
RxLog
RxLog
ACK
RxLog
TxLog
RxLog

## Slide 20: WLAN Watch - Statistics
TRAFFIC PARAMETERS: SPECIFIED TRAFFIC COUNT: 3000
TRAFFIC PARAMETERS: UDP PACKET BODY (IN BYTES): 1000
RxLog: TOTAL PACKETS SNIFFED : 2700
RxLog: TOTAL CORRUPTED PACKETS : 40
RxLog: DUPLICATE PACKET : 502
RxLog: DUPLICATE PACKET : 1130
RxLog: DUPLICATE PACKET : 1144
RxLog: DUPLICATE PACKET : 1162
RxLog: DUPLICATE PACKET : 1629
RxLog: DUPLICATE PACKET : 1722
RxLog: TOTAL DUPLICATES FOUND : 6
RxLog: TOTAL PACKETS LOST : 349

## Slide 21: WLAN Watch – Statistics
RxLog: ERROR RATE - PERCENTAGE : 1.48
RxLog: PACKET LOSS - PERCENTAGE : 11.63
RxLog: THROUGHPUT : 1804. Kbps

## Slide 22: Traffic – Parameters
Destination IP
Source Port
Destination Port
PACKET_DATA_SIZE
SEQNO_START
SEQNO_SIZE
SEQNO_REDUNDANCY
TRAFFIC_COUNT
PACKET_CONTENT
PACKET HEADER
PACKET BODY
TRAFFIC

## Slide 23: Traffic - Format
000123
000123
000123
000123
PACKET_DATA_SIZE = 100
SEQNO_START = 123
SEQNO_SIZE = 6
SEQNO_REDUNDANCY = 4
….. abcxyz ..…
100 – (4*6)
SEQNO
SIZE

## Slide 24: WLAN Watch - Experiments
AP
Server
Client
CS316
CS315
CS314
Stairs
Lift
Lab
CS319
Water
Glass
Wall

## Slide 25: Information From RxLog
Per Packet Signal Level.
Count of packets.
Count of corrupted packets.
Count of uncorrupted packets.
Percentage of corrupted packets.
Percentage of uncorrupted packets.

## Slide 26: Plotting Graphs…
Corrupted Packets
Signal Level Interval | % of Traffic
0-4 | 0.00
5-9 | 3.21
10-14 | 4.38
… | ...
150-155 | 1.06
Uncorrupted Packets
Signal Level Interval | % of Traffic
0-4 | 0.00
5-9 | 0.00
10-14 | 17.92
…… | …..
150-155 | 22.06

## Slide 27: WLAN Watch - Features
Generic
  Supports Prism-II & Cisco Aironet cards.
GUI to configure the cards
  Specify the driver to be loaded.
  Associate with a given Access Point in infrastructure mode.
  Setup:
    IP Address,
    Netmask,
    Gateway,
    Route.

## Slide 28: WLAN Watch - Features
Sniffing
  Change the sniffing channel.
  Log the sniffed packets.
  Signal level and noise level of each sniffed packet.
Traffic Tuning
  Change packet size, Sequence number redundancy…
  Traffic Count.
  Traffic Contents.

## Slide 29: WLAN Watch - Features
Statistics
  Per Packet Signal Level.
  Per Packet Noise Level.
  Packet loss in Rx.
  Packets corrupted in Rx.
  Packets duplicated in Rx (along with their sequence numbers).
  Throughput.
Platform for conducting other experiments

## Slide 30: Forward Direction
Implementing forward error correction
Effect of co-channel interference on
  Error rate
  Packet loss
  Signal level
  Noise level
  Throughput

## Slide 31: Forward Direction
Effect of transmission rate on
  Error rate
  Packet loss
  Throughput
Effect of distance on
  Signal level
  Error rate
  Packet loss
  Throughput

## Slide 32: Forward Direction
Effect of packet size on
  Error rate
  Packet loss
  Throughput
Effect of mobility on
  Error rate
  Packet loss
  Signal level
  Throughput

## Slide 33: Forward Direction
Optimally setting up the APs
  Maximum coverage
  Maximum throughput
  Minimum interference

## Slide 34
Thank you