## Slide 1: Fastlane: A framework for building fast path network applications
Debojeet Das, Lakshya, Mythili Vutukuru
Systems and Networking Research Group (SynerG)
Department of CSE, IIT Bombay
10th IEEE NFV-SDN '24
Natal, Brazil, Nov 2024
Notes: Good afternoon everyone. In this talk, I will present to you Fastlane which is a new framework that we can use to easily build high performance network applications. This is a joint work with Lakshya and Mythili Vutukuru.

## Slide 2: High performance Network IO and the OS
Packet copying
Context switching
Kernel data structure allocation
Processing overheads increase with containers
NFs easier to develop with the socket interface
Kernel network stack is too slow for high-performance Network Functions (NFs)
NIC
Driver
Host N/W stack
Socket
NF in host
User space
Kernel space
NF in container
Socket
Container N/W stack
Notes: Why do we need high performance network I/O framework?
High-speed applications need to process massive amounts of traffic at high speeds. However, using the traditional kernel network stack for this is too slow because of multiple overheads like packet copying, context switching, and kernel data structure allocations, all of which can severely impact performance more so when deployed in containerized environments.
While it’s easy to write network functions using traditional socket interfaces, this approach just isn’t fast enough to handle modern high-performance needs of network functions. -- longer version As we all know the kernel implements the network stack and it interacts with the driver to deliver packets into NF through a socket interface. This generalized way of handling packets can be used in any scenario. But the kernel network stack is very slow for handling packets required for high performance network functions. The reason for the same being packet copies, context switches, kernel data structure allocations and so on. Moreover, when the NFs are deployed inside a container the overheads increase, as multiple network stack traversal is required for packet delivery. Keeping the problems aside. The benefits of using the traditional network stack is the ease that it provides to build a NF. Moreover, most of the legacy applications are built over traditional network stack only.

## Slide 3: High performance network IO frameworks
NF in host/container
User space
Kernel space
NIC
CNDP Library
Socket
Driver
XDP
NF in host/container
User space
Kernel space
NIC
DPDK Library
Data Path Development Kit (DPDK)
Kernel Bypass using user-space polling
Cloud Native Data Plane (CNDP) Kernel Bypass using eBPF XDP hook
Zero Copy
Reduced context switches
N/W stack has no control over NIC
Application rewrite is required
Zero Copy
Traditional N/W stack can use NIC
Application rewrite is required
Notes: To tackle these limitations, high-performance network I/O frameworks like DPDK and CNDP are widely used.
Data Plane Development Kit or DPDK bypasses the kernel stack altogether, allowing direct packet access with busy polling in user space, although this improves performance it has many disadvantages for example the kernel network stack can’t interact with the NIC therefore you can’t use tools like ethtool, iproute tools etc.
On the other hand, there is Cloud Native Data Plane or CNDP which is an alternative to DPDK that uses eBPF with a zero-copy XDP hook to redirect packets to userspace, bypassing further kernel processing. This approach allows the network stack to still have control over the NIC, unlike DPDK.
But to use these frameworks the applications needs to re-written using their required libraries which is a big problem for developers.

## Slide 4: DPDK vs. CNDP
DPDK outperforms CNDP in terms of throughput
For Performance DPDK
For Efficiency CNDP
CNDP’s CPU utilization is proportional to load
Notes: But which framework should a developer use?
.As we can see from the plots. Since, DPDK uses user-space polling mode driver to configure, control and receive/transmit packets in userspcace it can perform more packet processing than CNDP which still relies on the kernel drive for doing the same.
On the other hand, since CNDP uses the kernel driver which allows the application to be more efficient in terms of CPU cycle usage. If we look at the plot we can see at low loads CNDP used very low CPU, whereas DPDK was always running at 100% CPU utilization. A simple rule that developers can follow will be to -
Go for DPDK if you need performance, or else
Go for CNDP if you need efficiency

## Slide 5: Requirements for high-performance NF development/porting
Current solutions for NF development are silos that address one challenge only Ease of development or Performance or Efficiency
For porting legacy applications to high performance packet I/O framework: - Learn and understand new framework - Re-engineer the application for the new framework.
Goal: Reduce developer effort for development/porting while achieving high performance
Application
In
Slow Path
Application in Fast Path
- Handles low speed traffic
- Network stack based - Can be legacy application
- For high-speed traffic
Notes: But, for a developer who is tasked to develop a high-performance NF the current solutions can either provide ease of development or performance or efficiency.
Moreover, when porting a legacy application, developers face the challenge of learning and understanding the new framework while also re-engineering applications originally designed for the traditional network stack.
Fastlane was designed to simplify this entire process. Our goal was to set up enable high-performance network functions while minimizing the development and configuration overhead for developers.
Fastlane achieves this by dividing each application into two parts:
A fast path for high-speed traffic
And a slow path that uses the traditional kernel network stack for handling low-speed traffic.
Although a developer can try to setup this design on their own, it can again make the developer go down the rabbit hole of learning, understanding, and re-enginerring the entire application. Fastlane eases the set up of this split-path approach, it allows developers to achieve high throughput while making the deployment easier and more adaptable to different network environments

## Slide 6: Fastlane design
Fast Path
Application
In
Slow Path
Packet I/O Framework (DPDK, CNDP)
- Packet I/O Framework can be switched between CNDP / DPDK - No code changes required in fast path or slow path
Fastlane Datapath
Fast path packet processor
Notes: Let’s take a look at Fastlane’s architecture.
The core of Fastlane consists of a fast path packet processor for handling high-speed traffic with DPDK or CNDP, a slow path that relies on the kernel stack to manage lower-priority traffic and the packet I/O framework interface, where you can switch between DPDK and CNDP based on the use case. The change in the underlying framework doesn’t require any modification in the applications.

## Slide 7: Fastlane system overview
Fast Path
Application
In
Slow Path
Packet I/O Framework (DPDK, CNDP)
A user needs to provide:
Fast path application logic
Application to run in slow path
Configuration JSON file
Fastlane Datapath
Fast path packet processor
Fast path application logic
{
"API": "dpdk",
"MODEL": "run-to-completion",
"cloud-deployment": true,
"fastpath-port-configuration": {
"fastpath-filtering": true,
"fastpath-ports": [
2152,]
},
}
. . .
Configuration JSON
JSON file contains:
- Framework to be used
- Baremetal or Cloud deployment
- Fast path filter rules
many more..
Notes: To get started the user has to provide a Fast path application logic and a slow path application.
Configuration is managed via JSON files, so you don’t need to modify the code for setup. This makes Fastlane flexible and easy to deploy across different environments.

## Slide 8: Fastlane packet processing flow
Fast path packet processor
Fast Path
Packet I/O Framework (DPDK, CNDP)
Application
In
Slow Path
1. Packet arrival
2. Inject packet
2. Run fast path
3. Verdict
4. Inject packet
4. Transmit the packet
5. Packet from application
Fastlane Datapath
How to handle packets that are sent from the slow path?
Verdicts: - NIC ports: To transmit the packet out through the NIC - Drop: To drop the packet ASAP - Kernel: To inject the packet to the slow path
Notes: Here’s how packet processing works in Fastlane. Packets arrive and are directed to either the fast path or the slow path based on application requirements. The fast path processes high-speed packets quickly, applying a 'verdict' to each packet which can be a NIC port to transmit the packet out of the NIC, Drop to drop the packet, or Kernel to send the packet to network stack for further processing in the slow path. This model allows Fastlane to make efficient use of resources, processing high-speed traffic in the fast path while managing less time-sensitive packets in the slow path.
But how to handle the packets originating from the slow path? These packets may need to be re-injected into the fast path for further processing or directly transmitted based on their updated requirements.

## Slide 9: Fastlane packet processing model
Fast path packet processor
Fast Path
Packet I/O Framework (DPDK, CNDP)
Verdicts: - NIC ports: To transmit the packet out through the NIC. - Drop: To drop the packet ASAP. - Kernel: To inject the packet to the slow path.
Application
In
Slow Path
1. Packet arrival
2. Inject packet
2. Run fast path
4. Inject packet
4. Transmit the packet
5. Packet from application
Fastlane Datapath
Handler
3. Verdict
6. Verdict
Notes: To tackle this Fastlane provides mechanisms to handle this flow using a handler, allowing packets processed in the slow path to either re-enter the fast path for additional processing or be sent to their destination efficiently using the verdict semantics of Fastlane. This seamless flow between paths ensures that all packets, regardless of origin or speed requirements, are handled with optimal resource allocation and processing speed.

## Slide 10: Fastlane implementation highlights
Fast path packet processor
Fast Path
TAP Processor
Application
In
Slow Path
Packet I/O Framework (DPDK, CNDP)
TAP
Shared Memory
Packet injection to the kernel is done using TAP device
TAP processor handles the packet sent from application
Shared Memory - for fast path-slow path interactions
Notes: Here we show the implementation of Fastlane We use a TAP device to handle packet injection to and from the kernel. We provide Shared memory and corresponding APIs to facilitate communication between the fast path and the slow path. The framework is designed to be highly modular, allowing developers to configure packet processing without rewriting application.
These elements ensure that Fastlane can process packets at high speed without forcing developers to redesign their entire application stack.

## Slide 11: Real world example – 5G UPF
UPF
SMF
NRF
. . . . . .
Control Plane Network Functions
5G Core Network
Data Network
Radio Access Network
GTP over UDP
PFCP over UDP
JSON over HTTP/TCP
User Device
Base Station
Notes: To illustrate how Fastlane works in a real-world scenario, let’s look at a case study involving a 5G User Plane Function, or UPF.
UPFs are critical in 5G as they handle data packet forwarding between user device and data network. UPF communicates with Control plane NFs using JSON over HTTP/TCP and PFCP over UDP. For the actual packet forwarding it uses GTP over UDP. The GTP processing happens at very high rate whereas the control plane packet come at low-rates but has higher complexity requiring complex parsing logic. Using the idea of slow path and fast path, we can implement the GTP handling as fast path and leave all other packet processing to slow path application

## Slide 12: Real world example – Fastlane 5G UPF
SMF
NRF
. . . . . .
Control Plane Network Functions
5G Core Network
Data Network
Radio Access Network
GTP over UDP
PFCP over UDP
JSON over HTTP/TCP
UPF
UPF
UPF running over kernel
network stack (slow path)
Fastlane UPF (fast path)
Fastlane interactions
User Device
Base Station
Notes: In our evaluation, we ported an existing 5G UPF which was built on top of kernel network stack to Fastlane. Here, the existing 5G UPF was modified to act as the slow path whereas a new fast path UPF was created which reuses the GTP (GPRS Tunneling Protocol) logic from the existing UPF implementation, which means we were able to build fast path network application without rewriting core application components.
This case study highlights Fastlane's ability to leverage existing code, making it possible to achieve high performance with minimal changes.

## Slide 13: UPF System setup details
DNN
UPF
RAN
NIC
Intel(R) Xeon(R) CPU E5-2670 v3 @ 2.30GHz, 128 GB RAM
Intel XL710 NICs (40 Gbps)
Ubuntu 22.04 (Linux kernel 5.15.0-25-generic)
10K user sessions
20K PDRs, 20K FARs
NIC
NIC
NIC
5G control plane
Notes: For our evaluation, we utilized a three-machine setup, with two machines configured as the RAN (Radio Access Network) and DNN (Data Network Node). The RAN was set up to handle 10,000 concurrent users, utilizing 20,000 PDRs (Packet Detection Rules) and 20,000 FARs (Forwarding Action Rules). All packets sent to the DNN were then forwarded back to the RAN, creating a continuous flow for testing and evaluation.

## Slide 14: Fastlane evaluation
Is Fastlane’s separation of fast path and slow path processing effective?
UPF over N/W stack << 1Mpps
UPF over N/W stack <<< Fastlane-DPDK
UPF over N/W stack << Fastlane-CNDP
Notes: Initially the Kernel based UPF was able to provide only 0.11 Mpps for 64B packets.
Whereas wen we used the ported UPF we were able to increase that by around 90 times incase of DPDK and 22 times incase of CNDP for 64B packets.
The difference of the performance between DPDK vs CNDP is to be expected as we discussed earlier.

## Slide 15: Fastlane evaluation
Is Fastlane’s separation of fast path and slow path processing effective?
Does Fastlane simplify the development efforts of fast path network applications?
Traditional UPF |  | Fastlane UPF*
Total LOC | Modified LOC | New LOC
4954 | 472 | 311
*Fastlane UPF reuses the GTP application logic of Traditional UPF

## Slide 16: Fastlane evaluation
Is Fastlane’s separation of fast path and slow path processing effective?
Does Fastlane simplify the development efforts of fast path network applications?
Can applications built using Fastlane deliver performance comparable to those developed natively with CNDP or DPDK?
Notes: we are adding in range of 0.2-5.5 us

## Slide 17: Fastlane evaluation
Is Fastlane’s separation of fast path and slow path processing effective?
Does Fastlane simplify the development efforts of fast path network applications?
Can applications built using Fastlane deliver performance comparable to those developed natively with CNDP or DPDK?
Are applications built with Fastlane scalable across multiple cores?

## Slide 18: Summary
Fastlane, a framework that ports the fast path of network applications to high-speed packet I/O frameworks, while keeping the slow path on the traditional network stack
Fastlane: - provides easy porting using split fast-path, slow-path design - no application re-writes due to its Packet I/O agnostic API - works in both baremetal and cloud
Looking ahead: - auto-scaling in cloud - runtime switching between DPDK and CNDP
Notes: To summarize, Fastlane provides a practical solution for porting fast-path applications to high-performance packet I/O frameworks while retaining the flexibility of the kernel stack.
Fastlane eases application development by dividing applications into fast and slow paths. It supports both DPDK and CNDP, giving developers flexibility depending on their requirements. It works well in both bare-metal and cloud deployment environments.
Looking ahead, we plan to introduce auto-scaling to Fastlane and enable runtime switching between DPDK and CNDP based on resource availability.

## Slide 19
Thank You!
Questions?
debojeetdas@cse.iitb.ac.in
Fastlane: A framework for building fast path network applications
Debojeet Das
Notes: Thank you for your attention. I’d be happy to take any questions you have.