## Slide 1: Kinectic vision
Prof. Partha Pratim Das, ppd@cse.iitkgp.ernet.in & partha.p.das@gmail.com
Department of Computer Science & Engineering
Indian Institute of Technology Kharagpur
Looking Deep into Depth
Tutorial: NCVPRIPG 2013
18th December 2013

## Slide 2
Natural Interaction
Understanding human nature
How we interact with other people
How we interact with environment
How we learn
Interaction methods the user is familiar and comfortable with
Touch
Gesture
Voice
Eye Gaze

## Slide 3
Gesture
Voice
Eye Gaze
Touch

## Slide 4
Notes: http://www.google.co.in/imgres?espv=210&es_sm=93&biw=1366&bih=624&tbm=isch&tbnid=wfnEl7vR6I9XMM:&imgrefurl=http://en.wikipedia.org/wiki/Natural_user_interface&docid=8iCRReaH83F3kM&imgurl=http://upload.wikimedia.org/wikipedia/en/7/7c/CLI-GUI-NUI.png&w=1310&h=652&ei=lt59Uv_fC4SRrAe7n4CQCQ&zoom=1&ved=1t:3588,r:3,s:0,i:92&iact=rc&page=1&tbnh=158&tbnw=318&start=0&ndsp=5&tx=235&ty=72

## Slide 5
Notes: http://www.google.co.in/imgres?start=103&espv=210&es_sm=93&biw=1366&bih=624&tbm=isch&tbnid=WLHUUs3mnYzdiM:&imgrefurl=http://www.xtremelabs.com/2013/08/the-future-of-uiux-the-natural-user-interface/&docid=S2ZkYOXSFNHfBM&imgurl=http://www.xtremelabs.com/wp-content/uploads/2013/07/futureUIUX1.jpg&w=600&h=300&ei=y959UubRNJGyrAeZiIGICA&zoom=1&ved=1t:3588,r:3,s:100,i:13&iact=rc&page=7&tbnh=159&tbnw=318&ndsp=20&tx=211&ty=70

## Slide 6
Natural User Interface
Revolutionary change in Human-Computer interaction
Interpret natural human communication
Computers communicate more like people
The user interface becomes invisible
or looks and feels so real that it is no longer iconic

## Slide 7: Three Layer NUI Model

## Slide 8: Layer 1: HCI – Devices and Software Detect and process human behavior

## Slide 9: Layer 2: NUI – Middleware and Application Framework Translate human behavior into action

## Slide 10: Layer 3: Ambient Computing – Orchestrate billions of devices NUI becomes part of everyday life

## Slide 11
Factors for NUI Revolution

## Slide 12: Factors for NUI Revolution
Sensor – Detect human behavior
NUI Middleware Libraries – Interprets human behavior
Cloud – Extend NUI across multiple device
Sensors
Libraries
Application
Cloud

## Slide 13: Point of Our Interest
Sensors
Libraries
Application

## Slide 14: Different Sensors
Touch
  Mobile Phones
  Tablets and Ultrabooks
  Portable Audio Players
  Portable Game Consoles
Touch Less
  RGB camera
  Depth camera – Lidar, CamBoard nano
  RGBD camera – Kinect, Asus Xtion pro, Carmine 1.08
  Eye tracker – Tobii eye tracker
  Voice recognizer – Kinect, Asus Xtion pro, Carmine 1.08

## Slide 15: Revolutionary – Kinect

## Slide 16: Revolutionary – Kinect
Low Cost

## Slide 17
Kinect
The most popular NUI Sensor

## Slide 18
It’s changing the way to play games
Full Body Gaming
It’s All About You
Something For Everyone
Notes: Full Body Gaming
Controller-free gaming means full body play. Kinect responds to how you move. So if you have to kick, then kick. If you have to jump, then jump. You already know how to play. All you have to do now is to get off the couch.
It’s All About You
Once you wave your hand to activate the sensor, your Kinect will be able to recognize you and access your Avatar. Then you'll be able to jump in and out of different games, and show off and share your moves.
Something For Everyone
Whether you're a gamer or not, anyone can play and have a blast. And with advanced parental controls, Kinect promises a gaming experience that's safe, secure and fun for everyone.

## Slide 19: controller FREE gaming
Notes: Simply step in front of the sensor and Kinect recognizes you and responds to your gestures.

## Slide 20: Amazing Games & APPS VIDEOs
Games / Apps
  Sports
  Dance/Music
  Fitness
  Family
  Action Adventure
Videos
  Xbox 360
  Fitnect
  Humanoid
  Magic Mirror

## Slide 21: Watch APPS VIDEOs
Xbox 360
  http://www.youtube.com/watch?v=_xLTI-b-cZU
Fitnect – Virtual Fitting Room
  http://www.openni.org/solutions/fitnect-virtual-fitting-room/
  http://www.fitnect.hu/
Controlling a Humanoid Robot with Kinect
  http://www.wimp.com/robotkinect/
Magic Mirror in Bathroom
  http://www.extremetech.com/computing/94751-the-new-york-times-magic-mirror-will-bring-shopping-to-the-bathroom

## Slide 22: What is Kinect?
Low-cost sensor device for providing real-time depth, color and audio data.

## Slide 23: How Kinect supports NUI?

## Slide 24: Hardware and Software Interaction

## Slide 25: SDK Architecture
Notes: Kinect hardware - The hardware components, including the Kinect sensor and the USB hub through which the Kinect sensor is connected to the computer.
Kinect drivers - The Windows drivers for the Kinect, which are installed as part of the SDK setup process as described in this document. The Kinect drivers support:
  The Kinect microphone array as a kernel-mode audio device that you can access through the standard audio APIs in Windows.
  Audio and video streaming controls for streaming audio and video (color, depth, and skeleton).
  Device enumeration functions that enable an application to use more than one Kinect
Audio and Video Components Kinect natural user interface for skeleton tracking, audio, and color and depth imaging
DirectX Media Object (DMO) for microphone array beam forming and audio source localization.
Windows 7 standard APIs - The audio, speech, and media APIs in Windows 7, as described in the Windows 7 SDK and the Microsoft Speech SDK. These APIs are also available to desktop applications in Windows 8.

## Slide 26: SDK Architecture
Kinect hardware - The hardware components, including the Kinect sensor and the USB hub through which the Kinect sensor is connected to the computer.
Kinect drivers - Windows drivers for the Kinect:
  Microphone array as a kernel-mode audio device –std audio APIs in Windows.
  Audio and video streaming controls (color, depth, and skeleton).
  Device enumeration functions for more than one Kinect
Audio and Video Components Kinect NUI for skeleton tracking, audio, and color and depth imaging
DirectX Media Object (DMO)
  microphone array beamforming
  audio source localization.
Windows 7 standard APIs - The audio, speech, and media APIs and the Microsoft Speech SDK.
Notes: Kinect hardware - The hardware components, including the Kinect sensor and the USB hub through which the Kinect sensor is connected to the computer.
Kinect drivers - The Windows drivers for the Kinect, which are installed as part of the SDK setup process as described in this document. The Kinect drivers support:
  The Kinect microphone array as a kernel-mode audio device that you can access through the standard audio APIs in Windows.
  Audio and video streaming controls for streaming audio and video (color, depth, and skeleton).
  Device enumeration functions that enable an application to use more than one Kinect
Audio and Video Components Kinect natural user interface for skeleton tracking, audio, and color and depth imaging
DirectX Media Object (DMO) for microphone array beam forming and audio source localization.
Windows 7 standard APIs - The audio, speech, and media APIs in Windows 7, as described in the Windows 7 SDK and the Microsoft Speech SDK. These APIs are also available to desktop applications in Windows 8.

## Slide 27: Hardware

## Slide 28: Main components

## Slide 29: Main components
RGB camera
Infrared (IR) emitter and an IR depth sensor – estimate depth
Multi-array microphone - four microphones for capturing sound.
3-axis Accelerometer - configured for a 2g range, where g is the acceleration due to gravity. Determines the current orientation of the Kinect.

## Slide 30: Interaction Space

## Slide 31: NUI API

## Slide 32: Four data streams
NUI API lets the user programmatically control and access four data streams.
Color Stream
Infrared Stream
Depth Stream
Audio Stream

## Slide 33: Stream APPs
Source: Kinect for Windows Developer Toolkit v1.8
  http://www.microsoft.com/en-in/download/details.aspx?id=40276
App Examples:
  Color Basics - D2D
  Infrared Basics - D2D
  Depth Basics - D2D / Depth - D3D
  Depth with Color - D3D
  Kinect Explorer - D2D
  Kinect Explorer - WPF

## Slide 34: COLOR Stream APPs
Source: Kinect for Windows Developer Toolkit v1.8
  http://www.microsoft.com/en-in/download/details.aspx?id=40276
App Examples:
  Color Basics - D2D

## Slide 35: Color stream
Color Format | Resolution
RGB | 640x480 Fps30
 | 1280x960 Fps12
YUV | 640x480 Fps15
Bayer | 640x480 Fps30
 | 1280x960 Fps12
New features of SDK 1.6 onwards:
Low light (or brightly lit).
Use hue, brightness, or contrast to improve visual clarity.
Use gamma to adjust the way the display appears on certain hardware.

## Slide 36: INFRARED Stream APPs
Source: Kinect for Windows Developer Toolkit v1.8
  http://www.microsoft.com/en-in/download/details.aspx?id=40276
App Examples:
  Infrared Basics - D2D

## Slide 37: Infrared stream
IR stream is the test pattern observed from both the RGB and IR camera
Resolution 640x480 Fps 30
Notes: There is only one color image stream available per sensor. The infrared image stream is provided by the color image stream, therefore, it is impossible to have a color image stream and an infrared image stream open at the same time on the same sensor.

## Slide 38: DEPTH Stream APPs
Source: Kinect for Windows Developer Toolkit v1.8
  http://www.microsoft.com/en-in/download/details.aspx?id=40276
App Examples:
  Depth Basics - D2D
  Depth - D3D
  Depth with Color - D3D

## Slide 39: Depth stream
The depth data stream merges two separate types of data:
  Depth data, in millimeters.
  Player segmentation data
    Each player segmentation value is an integer indicating the index of a unique player detected in the scene.
    The Kinect runtime processes depth data to identify up to six human figures in a segmentation map.

## Slide 40: Depth stream

## Slide 41: AUDIO Stream APPs
Source: Kinect for Windows Developer Toolkit v1.8
  http://www.microsoft.com/en-in/download/details.aspx?id=40276
App Examples:
  Kinect Explorer - D2D
  Kinect Explorer - WPF

## Slide 42: Audio stream
High-quality audio capture
Audio input from + and – 50 degree in front of sensor
The array can be pointed at 10 degree increment with in the range
Identification of the direction of audio sources
Raw voice data access
Notes: The beamforming functionality supports 11 fixed beams, which range from -0.875 to 0.875 radians (approximately -50 to 50 degrees in 10-degree increments). Applications can use the DMO’s adaptive beamforming option, which automatically selects the optimal beam, or specify a particular beam. The DMO also includes a source localization algorithm, which estimates the source direction.

## Slide 43: Audio stream

## Slide 44: runtime implements
In addition to the hardware capabilities, the Kinect software runtime implements:
Skeleton Tracking
Speech Recognition - Integration with the Microsoft Speech APIs.

## Slide 45: Skeleton tracking

## Slide 46: Skeleton tracking APPS
Source: Kinect for Windows Developer Toolkit v1.8
  http://www.microsoft.com/en-in/download/details.aspx?id=40276
App Examples:
  Skeleton Basics - D2D
  Kinect Explorer - D2D
  Kinect Explorer - WPF

## Slide 47: Skeleton tracking
Tracking Modes (Seated/Default)
Tracking Skeletons in Near Depth Range
Joint Orientation
Joint Filtering
Skeleton Tracking With Multiple Kinect Sensors

## Slide 48: Speech Recognition APPS
Source: Kinect for Windows Developer Toolkit v1.8
  http://www.microsoft.com/en-in/download/details.aspx?id=40276
App Examples:
  Speech Recognition - Integration with the Microsoft Speech APIs.
    Speech Basics - D2D
    Tic-Tac-Toe - WPF

## Slide 49: Speech Recognition
Microphone array is an excellent input device for speech recognition.
Applications can use Microsoft.Speech API for latest acoustical algorithms.
Acoustic models have been created to allow speech recognition in several locales in addition to the default locale of en-US.

## Slide 50: Additional libraries & APIs
Face Tracking
Kinect Fusion
Kinect Interaction

## Slide 51: Face Tracking Apps
Source: Kinect for Windows Developer Toolkit v1.8
  http://www.microsoft.com/en-in/download/details.aspx?id=40276
App Examples:
  Face Tracking 3D - WPF
  Face Tracking Basics - WPF
  Face Tracking Visualization

## Slide 52: Face tracking
Input Images
The Face Tracking SDK accepts Kinect color and depth images as input. The tracking quality may be affected by the image quality of these input frames
Face Tracking Outputs
Tracking status
2D points
3D head pose
Action Units (Aus)
Notes: The Face Tracking SDK uses the Kinect coordinate system to output its 3D tracking results. The origin is located at the camera’s optical center (sensor), Z axis is pointing towards a user, Y axis is pointing up. The measurement units are meters for translation and degrees for rotation angles.

## Slide 53: Face tracking
2D points
Notes: The Face Tracking SDK tracks the 87 2D points indicated in the following image (in addition to 13 points that aren’t shown in Figure 2 - Tracked Points):

## Slide 54: Face tracking
3D head pose
Notes: The X,Y, and Z position of the user’s head are reported based on a right-handed coordinate system (with the origin at the sensor, Z pointed towards the user and Y pointed UP – this is the same as the Kinect’s skeleton coordinate frame). Translations are in meters.
The user’s head pose is captured by three angles: pitch, roll, and yaw.

## Slide 55: Face tracking
AUs
AU0 – Upper Lip Raiser
AU1 – Jaw Lowerer
AU2 – Lip Stretcher
AU3 – Brow Lowerer
Notes: The Face Tracking SDK results are also expressed in terms of weights of six AUs and 11 SUs, which are a subset of what is defined in the Candide3 model (http://www.icg.isy.liu.se/candide/). The SUs estimate the particular shape of the user’s head: the neutral position of their mouth, brows, eyes, and so on. The AUs are deltas from the neutral shape that you can use to morph targets on animated avatar models so that the avatar acts as the tracked user does.
The Face Tracking SDK tracks the following AUs. Each AU is expressed as a numeric weight varying between -1 and +1.

## Slide 56: Kinect Fusion Apps
Source: Kinect for Windows Developer Toolkit v1.8
  http://www.microsoft.com/en-in/download/details.aspx?id=40276
App Examples:
  Kinect Fusion Basics - D2D
  Kinect Fusion Color Basics - D2D
  Kinect Fusion Explorer - D2D

## Slide 57: Kinect Fusion
Take depth images from the Kinect camera with lots of missing data
Within a few seconds producing a realistic smooth 3D reconstruction of a static scene by moving the Kinect sensor around.
From this, a point cloud or a 3D mesh can be produced.

## Slide 58: Kinect Fusion

## Slide 59: Kinect Interaction Apps
Source: Kinect for Windows Developer Toolkit v1.8
  http://www.microsoft.com/en-in/download/details.aspx?id=40276
App Examples:
  Interaction Gallery - WPF

## Slide 60: Kinect Interaction
Kinect Interaction provides:
Identification of up to 2 users and identification and tracking of their primary interaction hand.
Detection services for user's hand location and state.
Grip and grip release detection.
Press and scroll detection.
Information on the control targeted by the user.
Notes: http://msdn.microsoft.com/en-us/library/dn188673.aspx

## Slide 61: Third Party Libraries

## Slide 62: Third Party Libraries
Matlab
OpenCV
PCL (Point Cloud Library)
BoofCV Library
ROS

## Slide 63: Matlab & OpenCV
Matlab is a high-level language and interactive environment for numerical computation, visualization, and programming.
Open Source Computer Vision (OpenCV) is a library of programming functions for real-time computer vision.
MATLAB and OpenCV functions perform numerical computation and visualization on video and depth data from sensor.
Source:
Maltlab – http://msdn.microsoft.com/en-us/library/dn188693.aspx
OpenCV – http://msdn.microsoft.com/en-us/library/dn188694.aspx
Notes: Maltlab – http://msdn.microsoft.com/en-us/library/dn188693.aspx
OpenCV - http://msdn.microsoft.com/en-us/library/dn188694.aspx

## Slide 64: PCL (Point Cloud Library)
Source: PCL – http://pointclouds.org/documentation/
Notes: http://pointclouds.org/documentation/
The Point Cloud Library (PCL) is a large scale, open project for point cloud processing.
The PCL framework contains numerous algorithms including filtering, feature estimation, surface reconstruction, registration, model fitting and segmentation. These algorithms can be used, for example, to filter outliers from noisy data, stitch 3D point clouds together, segment relevant parts of a scene, extract keypoints and compute descriptors to recognize objects in the world based on their geometric appearance, and create surfaces from point clouds and visualize them – to name a few.
PCL is cross-platform, and has been successfully compiled and deployed on Linux, MacOS, Windows, and Android.
To simplify development, PCL is split into a series of smaller code libraries, that can be compiled separately

## Slide 65: Ros (Robot Operating System)
Provides libraries and tools to help software developers create robot applications.
Provides hardware abstraction, device drivers, libraries, visualizers, message-passing, package management, and more.
Provides additional RGB-D processing capabilities.
Source: ROS – http://wiki.ros.org/openni_camera
Notes: http://wiki.ros.org/openni_camera

## Slide 66: BoofCV
Depth image from Kinect sensor
3D point cloud created from RGB & depth images
Binary Image processing
Image registration and model fitting
Interest point detection
Camera calibration
Provides RGB-D processing capabilities.
Source: BoofCV – http://boofcv.org/index.php?title=Tutorial_Kinect
Notes: http://boofcv.org/index.php?title=Tutorial_Kinect
http://www.codeproject.com/Articles/293269/BoofCV-Real-Time-Computer-Vision-in-Java

## Slide 67: Applications

## Slide 68: Kinect Applications
Gesture Recognition
Gait Detection
Activity Recognition

## Slide 69: Gesture Recognition
Body Parts | Gestures | Applications | References
Fingers | 9 hand Gestures for number 1to 9 | Sudoku game | Ren et al. 2011
Hand, Fingers | Pointing gestures: pointing at objects or locations of interest | Real-time hand gesture interaction with the robot. Pointing gestures translated into goals for the robot. | Bergh et al. 2011
Arms | Lifting both arms to the front, to the side and upwards | Physical rehabilitation | Chang 2011
Hand | 10 hand Gestures for number 1 to 10 | HCI system. Experimental datasets in-clude hand signed digits gestures but framework can be generalized to recognize a wider range of gestures. | Doliotis 2011

## Slide 70: Gesture Recognition
Body Parts | Gestures | Applications | References
Hand and Head | Clap, Call, Greet, Yes, No, Wave, Clasp, Rest | HCI applications. Not build for any specic application | Biswas 2011
Single Hand | Grasp and Drop | Various HCI applications | Tang 2012
Right hand (default), Left hand, Head, Foot or Knee | Push, Hover | View and select recipes for cooking in Kitchen when hands are messy | Panger 2012
Hand, Arms | Right / Left-arm swing, Right / Left-arm push, Right / Left-arm back, Zoom-in/out | Various HCI applications. Not build for any specific application | Lai 2012

## Slide 71
Left and right swipe
Image source : Kinect for Windows Human Interface Guidelines v1.5
End presentation
Start presentation
Push gesture
Circling gesture
Hand as a
marker
Image source : Kinect for Windows Human Interface Guidelines v1.5
POWERPOINT PRESENTATION CONTROL from hand gesture

## Slide 72
Gesture path
Right swipe gesture paths
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 73
Consider an example : Take a left swipe path
The sequence of angles will be of the form [180,170,182, … ,170,180,185]
The corresponding quantized feature vector is [9,9,9, … , 9,9,9]
How does it distinguish left swipe from right swipe? Very straightforward!
MODELING GESTURES
Chart: 

## Slide 74
MACHINE LEARNING
Returns likelihoods which are then converted to probabilities by normalization, followed by thresholding (empirical) to classify gestures
HMM model for left swipe
HMM model for right swipe
HMM model for push
Real time gesture
L1
L2
L3
L4

## Slide 75
Here are the results obtained by the implementation
Precision = 97.23 %
Recall = 93.66 %
F-measure = 95.41 %
Accuracy = 95.5 %
RESULTS
 | Correct Gesture | Incorrect gesture
Correctly classified | 281 | 8
Wrongly classified | 19 | 292

## Slide 76: Human Gait Recognition Using Depth Camera: A Covariance Based Approach
Source: http://www.serc.iisc.ernet.in/~venky/Papers/Kinect_gait.pdf
Notes: http://www.serc.iisc.ernet.in/~venky/Papers/Kinect_gait.pdf

## Slide 77: Human Gait Recognition Using Depth Camera: A Covariance Based Approach
(a) Fixed Camera (b) Freely moving camera
Recognition Rate – 97%

## Slide 78: Team Activity Analysis and Recognition Based on Kinect Depth Map and Optical Imagery Techniques
Source: http://www.tnstate.edu/itmrl/documents/Team%20Activity%20Analysis.pdf
Notes: http://www.tnstate.edu/itmrl/documents/Team%20Activity%20Analysis.pdf

## Slide 79: Windows SDK vis-à-vis OpenNI

## Slide 80: Kinect SDK vis-à-vis OpenNI
Library | Capture | Process | Sensor | Platform
OpenNI | Yes | Yes | Primesense Sensors | Windows/ MacOS/ Linux
Kinect for Windows SDK | Yes | Yes | Kinect | Windows and VM
Factors | Kinect SDK | OpenNI
Depth Range | 0.8m – 4.0m | 0.5m – 9m
Skeleton Joints | 20 joints | 15 joints
Too near Too far index | Yes | No

## Slide 81: Kinect SDK vis-à-vis OpenNI
Skeleton Tracking
KinectInteraction
Kinect Fusion
Face Tracking
NITE
3D Hand
KSCAN3D
3-D FACE
Additional libraries and APIs
OpenNI Middleware
Source:
NITE – http://www.openni.org/files/nite/
3D Hand – http://www.openni.org/files/3d-hand-tracking-library/
3D face – http://www.openni.org/files/3-d-face-modeling/
KSCAN3D – http://www.openni.org/files/kscan3d-2/
Notes: NITE - http://www.openni.org/files/nite/
3D Hand - http://www.openni.org/files/3d-hand-tracking-library/
3D face - http://www.openni.org/files/3-d-face-modeling/
KSCAN3D - http://www.openni.org/files/kscan3d-2/

## Slide 82: Application in openni
Evaluating a Dancer’s Performance using Kinect-based Skeleton Tracking
Joint Positions
Joint Velocity
3D Flow Error
Source: http://doras.dcu.ie/16574/1/ACMGC_Doras.pdf
Notes: http://doras.dcu.ie/16574/1/ACMGC_Doras.pdf

## Slide 83: Kinect SDK vis-à-vis OpenNI
Better skeleton representation
20 joints skeleton
Joints are mobile
Higher frame rate – better for tracking actions involving rapid pose changes
Significantly better skeletal tracking algorithm (by Shotton, 2013). Robust and fast tracking even in complex body poses
Simpler skeleton representation
15 joints skeleton
Fixed basic frame of [shoulder left: shoulder right: hip] triangle and [head:shoulder] vector
Lower frame rate – slower tracking of actions
Weak skeletal tracking.
Kinect SDK
OpenNi

## Slide 84: How does kinect works

## Slide 85: Depth Sensing

## Slide 86: How pattern looks like?

## Slide 87: Depth sensing
The IR emitter projects an irregular pattern of IR dots of varying intensities.
The IR camera reconstructs a depth image by recognizing the distortion in this pattern.
Kinect works on stereo matching algorithm. It captures stereo with only one IR camera.

## Slide 88: Depth sensing
Project Speckle pattern onto the scene
Infer depth from the deformation of the Speckle pattern

## Slide 89: Skeleton Tracking

## Slide 90: pose estimation pipeline
capture depth image & remove background
infer body parts
per pixel
cluster pixels to
hypothesize body joint positions
fit model &
track skeleton

## Slide 91: Body part Inference
Highly varied training dataset - driving, dancing, kicking, running, navigating menus, etc (500k images)
The pairs of depth and body part images - used for learning the classifier.
Randomized decision trees and forests - used to classify each pixel to a body part based on some depth image feature and threshold
Notes: Highly varied training dataset allows the classifier to estimate body parts invariant to pose, body shape, clothing, etc. (500k images)
The pairs of depth and body part images are used as fully labelled data for learning the classifier.
Randomized decision trees and forests are used to classify each pixel to a body part based on some depth image feature and threshold

## Slide 92: Joint position proposals
Find joint point in each body parts - local mode-finding approach based on mean shift with a weighted Gaussian kernel.
This process considers both the inferred body part probability at the pixel and the world surface area of the pixel.

## Slide 93: Results
Input Depth
Inferred body parts
Front view
Side view
Top view
Inferred body joint position
No tracking or smoothing

## Slide 94: Using multiple kinects

## Slide 95: Pros & Cons of Kinect
Multimedia Sensor
Ease of Use
Low Cost
Strong Library Support
2.5D depth data
Limited field of view
  43o vert, 57o horz
Limited Range
  0.8 – 3.5 m
Uni-Directional View
Depth Shadows
Limited resolution
Missing depth values
PROS
CONS

## Slide 96: Limited Space for an actor
For a single Kinect, minimum of 10 feet by 10 feet space (3 meters by 3 meters) is needed.
Side View
Top View

## Slide 97: Depth Shadow

## Slide 98: Solution
Use Multiple Kinects

## Slide 99: Use of multiple kinect
3600 Reconstruction

## Slide 100: Use of multiple Kinect
Increases field of view
Super Resolution

## Slide 101: Drawbacks of Multiple Kinects
IR Interference Noise

## Slide 102: Multiple Kinects interference
Individual capture
Simultaneous capture
Difference

## Slide 103: Estimation of Noise
Estimate interference noise in 2 configuration
Parallel
Perpendicular
Perpendicular
Parallel

## Slide 104: Interference Noise
Single Kinect
Dual Kinects

## Slide 105: Interference Noise
Parallel
Perpendicular

## Slide 106: Estimators
Noise Measure | Angle (0) | Scene | Single Kinect | Two Kinects
% ZD Error | 180 | Room | 6.92 | 10.93
 | 180 | Human | 4.01 | 8.25
 | 90 | Human | 4.01 | 7.40
Avg (dmax - dmin) | 180 | Room | 329 | 639
 | 180 | Human | 206 | 624
 | 90 | Human | 206 | 408
Average Standard Deviation | 180 | Room | 89.15 | 185.71
 | 180 | Human | 58.26 | 168.91
 | 90 | Human | 58.26 | 118.65
% Pixels with dmin = 0 & dmax > 0 | 180 | Room | 8.08% | 17.52%
 | 180 | Human | 5.32% | 19.84%
 | 90 | Human | 5.32% | 11.87%

## Slide 107: Approaches to minimize interference
SDM: Space Division Multiplexing
  Circular Placement
  Axial and Diagonal Placement
  Vertical Placement
TDM: Time Division Multiplexing
  Mechanical Shutter (TDM-MS)
  Electronic Shutter (TDM-ES)
  Software Shutter (TDM-SS)
PDM: Pattern Division Multiplexing
  Body-Attached Vibrators
  Stand-Mounted Vibrators

## Slide 108: SDM – Circular Placement

## Slide 109: SDM – Circular Placement

## Slide 110: SDM – Circular Placement
Top View
Side View

## Slide 111: SDM – Axial and Diagonal Placement

## Slide 112: SDM – Axial and Diagonal Placement
Top View
Side View

## Slide 113: SDM – Vertical Placement

## Slide 114: TDM - Mechanical Shutter (TDM-MS)
Moving Shaft Shutter
Shutter Closed
Shutter Open

## Slide 115: TDM - Mechanical Shutter (TDM-MS)
A Revolving Disk Shutter

## Slide 116: TDM - Mechanical Shutter (TDM-MS)
4-phase Mechanical Shuttering

## Slide 117: TDM - Electronic Shutter (TDM-ES)

## Slide 118: TDM - Software Shutter (TDM-SS)
Microsoft's Kinect SDK v1.6 has introduced a new API (KinectSensor.ForceInfraredEmitterOff) to control the IR emitter as a Software Shutter.
  This API works for Kinect for Windows only.
Earlier the IR emitter was always active when the camera was active. Using this API the IR emitter can be put o as needed.
This is the most effective TDM scheme. However, no multi-Kinect application has yet been reported with TDM-SS.

## Slide 119: PDM – Body-Attached Vibrators

## Slide 120: PDM – Stand-Mounted Vibrators

## Slide 121: Comparison of Multiplexing Technique
Quality Factor | SDM | TDM | PDM
Accuracy | Excellent | Bad | Very Good
Scalability | Good (no overlaps) | Bad | Excellent
Frame rate | 30 fps | 30/n fps | 30 fps
Ease of Use | Very easy | Cumbersome shutters | Inconvenient vibrators
Cost | Low | High | Moderate
Limitations | Few configurations | Unstable | Blurred RGB
Robustness | Change Geometry | Adjust Set-up | Quite robust

## Slide 122: Buying the right kinects

## Slide 123: Which Kinect to buy?
Kinect for Xbox 360 –
  The gaming console of Xbox. Costs around $100 without the Xbox
  http://www.xbox.com/en-IN/Kinect
  Kinect Windows SDK is partially supported for this
Kinect for Windows –
  This is for Kinect App development. Costs around $250
  http://www.microsoft.com/en-us/kinectforwindows/
  Kinect Windows SDK is fully supported for this
Good for Gaming
Recommended for Research

## Slide 124: References
Ren, Z., Meng, J., and Yuan, J. Depth camera based hand gesture recognition and its applications in human-computer-interaction. In Information, Communications and Signal Processing (ICICS) 2011 8th International Conference on (2011), pp. 1- 5.
Biswas, K. K., and Basu, S. K. Gesture recognition using Microsoft Kinect. In Proceedings of the 5th International Conference on Automation, Robotics and Applications (2011), pp. 100 - 103.
Chang, Y.-J., Chen, S.-F., and Huang, J.-D. A Kinect-based system for physical rehabilitation: A pilot study for young adults with motor disabilities. Research in Developmental Disabilities (2011), 25662570.
Doliotis, P., Stefan, A., McMurrough, C., Eckhard, D., and Athitsos, V. Comparing gesture recognition accuracy using color and depth information. In Proceedings of the 4th International Conference on PErvasive Technologies Related to Assistive Environments, PETRA '11 (2011).

## Slide 125: References
Lai, K., Konrad, J., and Ishwar, P. A gesture-driven computer interface using kinect. In Image Analysis and Interpretation (SSIAI), 2012 IEEE Southwest Symposium on (2012), pp. 185 - 188.
Panger, G. Kinect in the kitchen: testing depth camera interactions in practical home environments. In CHI '12 Extended Abstracts on Human Factors in Computing Systems (2012), pp. 1985 - 1990.
Tang, M. Recognizing hand gestures with Microsoft’s Kinect. Department of Electrical Engineering, Stanford University.
Ahmed, N. A system for 360 acquisition and 3D animation reconstruction using multiple RGB-D cameras. Unpublished article. 2012.
  URL: http://www.mpiinf.mpg.de/~nahmed/casa2012.pdf.

## Slide 126: References
Caon, M., Yue, Y., Tscherrig, J., Mugellini, E., and Khaled, O. A. Contextaware 3D gesture interaction based on multiple Kinects. In Ambient Computing, Applications, Services and Technologies, Proc. AMBIENT First Int'l. Conf. on, pages 7-12, 2011.
Berger, K., Ruhl, K., Albers, M., Schroder, Y., Scholz, A., Kokemuller, J., Guthe, S., and Magnor, M. The capturing of turbulent gas flows using multiple Kinects. In Computer Vision Workshops, IEEE Int'l. Conf. on, pages 1108-1113, 2011a.
Berger, K., Ruhl, K., Brmmer, C., Schroder, Y., Scholz, A., and Magnor, M. Markerless motion capture using multiple color-depth sensors. In Vision, Modeling and Visualization, Proc. 16th Int'l. Workshop on, pages 317-324, 2011b.
Faion, F., Friedberger, S., Zea, A., and Hanebeck, U. D. Intelligent sensor scheduling for multi-Kinect-tracking. In Intelligent Robots and Systems (IROS), IEEE/RSJ Int'l. Conf. on, pages 3993-3999, 2012.

## Slide 127: References
Butler, A., Izadi, S., Hilliges, O., Molyneaux, D., Hodges, S., and Kim, D. Shake'n'Sense: Reducing interference for overlapping structured light depth cameras. In Human Factors in Computing Systems, Proc. ACM CHI Conf. on, pages 1933-1936, 2012.
Kainz, B., Hauswiesner, S., Reitmayr, G., Steinberger, M., Grasset, R., Gruber, L., Veas, E., Kalkofen, D., Seichter, H., and Schmalstieg, D. (2012). OmniKinect: Real-time dense volumetric data acquisition and applications. In Virtual reality software and technology, Proc. VRST'12: 18th ACM symposium on, pages 25-32, 2012.
Maimone, A. and Fuchs, H Reducing interference between multiple structured light depth sensors using motion. In Virtual Reality, Proc. IEEE Conf. on, pages 51-54, 2012.
Kramer, J., Burrus, N., Echtler, F., C., D. H., and Parker, M. Hacking the Kinect. Apress, 2012.

## Slide 128: References
Zelnik-Manor, L. & Or–El, R. Kinect Depth Map, Seminar in “Advanced Topics in Computer Vision” (048921 –Winter 2013). URL: http://webee.technion.ac.il/~lihi/Teaching/2012_winter_048921/PPT/Roy.pdf
iPiSoft Wiki. User Guide for Dual Depth Sensor Configurations. Last accessed 17-Dec-2013.
  URL: http://wiki.ipisoft.com/User_Guide_for_Dual_Depth_Sensor_Configuration
Tong, J., Zhou, J., Liu, L., Pan, Z., and Yan, H. (2012). Scanning 3D full human bodies using Kinects. Visualization and Computer Graphics, IEEE Transactions on, 18:643-650, 2012.
Mallick, T., Das, P.P., Majumdar, A. Study of Interference Noise in Multi-Kinect Set-up, Accepted for presentation at VISAPP 2014: 9th Int’l Jt. Conf. on Computer Vision, Imaging and Computer Graphics Theory and Applications, Lisbon, Portugal, 5-8, Jan, 2014.

## Slide 129: References
Huawei/3DLife ACM Multimedia Grand Challenge for 2013. http://mmv.eecs.qmul.ac.uk/mmgc2013/
Schroder, Y., Scholz, A., Berger, K., Ruhl, K., Guthe, S., and Magnor, M. Multiple Kinect studies. Technical Report 09-15, ICG, 2011.

## Slide 130: Credits
Tanwi Mallick, TCS Research Scholar, Department of Computer Science and Engineering, IIT, Kharagpur has prepared this presentation.

## Slide 131: Thank you